PART 1	GENERAL

1.1	SUMMARY

- Provide all equipment and materials, and do all work necessary to furnish and install the Track & Field Equipment, as indicated on the drawings and as specified herein.

1.2	RELATED WORK

- Examine Contract Documents for requirements that affect work of this section.  Other specification sections that directly relate to work of this Section include, but are not limited to:

  - Section 02200 - Earthwork; Excavation and Backfill and establishment of subgrade elevations.

  - Section 02511 - Asphalt Concrete Pavement

  - Section 02535 - Synthetic Track Surfacing

  - Section 02542 - Synthetic Field Surfacing

  - Section 03300 - Cast-in-Place Concrete; Concrete foundations and bases for goals.

1.3		REFERENCES

- Comply with applicable requirements of the following standards.  Where these standards conflict with other specified requirements, the most restrictive requirements shall govern.

      - U.S. Tennis Court and Track Builders Association

      - National Federation of State High School Associations (NFSHSA)

      - National Collegiate Athletic Association (NCAA)

      - International Amateur Athletic Foundation (I.A.A.F.)

      - Manufacturers Data and Recommended Installation Requirements.

1.4		SUBMITTALS

- Manufacturers Product Data

            - Provide manufacturer’s product literature, technical specifications and other data prior to actual field installation work for Architect or Owner’s Representative review.

# Shop Drawings

  - Provide drawings of manufacturers recommended installation and foundation requirements prior to actual field installation work for Architect or Owner’s Representative review.

1.5		QUALITY ASSURANCE

- Manufacturers warranties shall pass to the Owner and certification made that the product materials meet all applicable grade trademarks or conform to industry standards and inspection requirements.

1.6	DELIVERY, STORAGE AND HANDLING

- Materials delivered to the site shall be examined for concealed damage or defects in shipping. Any defects shall be noted and reported to the Owner’s Representative.

- Replacements, if necessary, shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- Sound materials shall be stored above the ground under protective cover or indoors so as to provide proper protection.

PART 2	PRODUCTS

2.1		MANUFACTURERS

- Manufacturers and product selections named are provided to establish the minimum standard.

      - Track & Field Equipment - As manufactured by AAE (Aluminum Athletic Equipment Co.); 1000 Enterprise Drive, Royersford, PA 19468; Toll Free (800) 523-5471.

2.2		MULTI-SPORT EQUIPMENT

- DONKEY™ (All Models: Sole Source) - Shall be as manufactured by AAE: ' "

  - Model # DONKEY-1™, Elevated Multi-Purpose Center: Portable Elevated Scoring Center/Press Box/Video Station/Officiating Center/Broadcast Booth for all sports; fully TIG welded 5' high elevated aluminum platform (bolted planks not accepted); surround completely TIG welded aluminum railing with 1-1/4"rd. aluminum spindles spaced 3-1/2" on center meets IBC Codes; fully portable unit with four (4) 16" diameter flat-free foam filled pneumatic wheel casters (two fixed, two swivel) with locking brakes; powder-coated front banner with customized school/club name and logo(s); TIG welded aluminum top canopy to be powder-coated in custom color provides protection from wind, weather and sun; seats six people comfortably, anodized aluminum bench seat and backrest slide forward and back, seat attached permanently to unit; powder-coated aluminum scorer’s table top 18" deep x 10' long provides a spacious area for computers and scorer’s accessories; durable mill-finish all-aluminum structural frame 4"sq. with .250" heavy-wall and rounded corners completely TIG welded sections; fluted mill-finish aluminum floor for additional traction and access ladder with safety handle; nominal dimensions are 11'H x 7'W x 11'L with an inside clearance (standing) of 6' 2" under top aluminum canopy; this model can be adapted with Model No. DONKEY-BN - Bird’s Nest Filming Platform

  - Model # DONKEY-2™, Elevated Multi-Purpose Center: Portable Elevated Scoring Center/Press Box/Video Station/Officiating Center/Broadcast Booth/Lockable Storage Compartment for all sports; fully TIG welded 5' high elevated aluminum platform (bolted planks not accepted); surround completely TIG welded aluminum railing with 1-1/4"rd. aluminum spindles spaced 3-1/2" on center meets IBC Codes; fully portable unit with four (4) 16" diameter flat-free foam filled pneumatic wheel casters (two fixed, two swivel) with locking brakes; powder-coated front banner with customized school/club name and logo(s); TIG welded aluminum top canopy to be powder-coated in custom color provides protection from wind, weather and sun; seats six people comfortably, anodized aluminum bench seat and backrest slide forward and back, seat attached permanently to unit; powder-coated aluminum scorer’s table top 18" deep x 10' long provides a spacious area for computers and scorer’s accessories; durable mill-finish all-aluminum structural frame 4"sq. with .250" heavy-wall and rounded corners completely TIG welded sections; fluted mill-finish aluminum floor for additional traction and access ladder with safety handle; nominal dimensions are 11'H x 7'W x 11'L with an inside clearance (standing) of 6' 2" under top aluminum canopy; this model can be adapted with Model No. DONKEY-BN - Bird’s Nest Filming Platformlockable storage unit underneath elevated scorer’s platform, approximately 160 cubic feet

  - Model # DONKEY-3™, Low-Profile Multi-Purpose Center: Portable Elevated Scoring Center/Press Box/Video Station/Officiating Center/Broadcast Booth for all sports; fully TIG welded 2’ high elevated aluminum platform (bolted planks not accepted); surround completely TIG welded aluminum railing with 1-1/4"rd. aluminum spindles spaced 3-1/2" on center meets IBC Codes; fully portable unit with four (4) 16" diameter flat-free foam filled pneumatic wheel casters (two fixed, two swivel) with locking brakes; powder-coated front banner with customized school/club name and logo(s); TIG welded aluminum top canopy to be powder-coated in custom color provides protection from wind, weather and sun; seats six people comfortably, anodized aluminum bench seat and backrest slide forward and back, seat attached permanently to unit; powder-coated aluminum scorer’s table top 18" deep x 10’ long provides a spacious area for computers and scorer’s accessories; durable mill-finish all-aluminum structural frame 4"sq. with .250" heavy-wall and rounded corners completely TIG welded sections; fluted mill-finish aluminum floor for additional traction and access ladder with safety handle; nominal dimensions are 9’H x 7’W x 11’L with an inside clearance (standing) of 6’ 2" under top aluminum canopy; this model cannot be adapted with Model No. DONKEY-BN - Bird’s Nest Filming Platform

  - Model # DONKEY-4™, Low-Profile Multi-Purpose Center: Portable Elevated Scoring Center/Press Box/Video Station/Officiating Center/Broadcast Booth for all sports; fully TIG welded 3' high elevated aluminum platform (bolted planks not accepted); surround completely TIG welded aluminum railing with 1-1/4"rd. aluminum spindles spaced 3-1/2" on center meets IBC Codes; fully portable unit with four (4) 16" diameter flat-free foam filled pneumatic wheel casters (two fixed, two swivel) with locking brakes; powder-coated front banner with customized school/club name and logo(s); TIG welded aluminum top canopy to be powder-coated in custom color provides protection from wind, weather and sun; seats six people comfortably, anodized aluminum bench seat and backrest slide forward and back, seat attached permanently to unit; powder-coated aluminum scorer’s table top 18" deep x 10' long provides a spacious area for computers and scorer’s accessories; durable mill-finish all-aluminum structural frame 4"sq. with .250" heavy-wall and rounded corners completely TIG welded sections; fluted mill-finish aluminum floor for additional traction and access ladder with safety handle; nominal dimensions are 10'H x 7'W x 11'L with an inside clearance (standing) of 6' 2" under top aluminum canopy; this model cannot be adapted with Model No. DONKEY-BN - Bird’s Nest Filming Platform

- DONKEY™ OPTIONAL ACCESSORIES - Shall be as manufactured by AAE:

(* typically specified items)

  - Model # DONKEY-BB, Back Banner (4' x 10'); 1/8" thick aluminum panel powder-coated in customers choice of color; includes one (1) color screen of school name or logo; attaches to back railing (can be added to any DONKEY model)

  - * Model # DONKEY-HA, Hitch Attachment with 2" ball coupler; allows unit to be towed by and vehicle with a 2" ball hitch (3mph max); 4' long galvanized steel square tube; galvanized steel/vinyl-coated black mounting plate with removable hinge pin allows for simple and convenient stow away

  - * Model # DONKEY-WS, Weather Screens, set of three (3) sides; 18oz. knife-coated vinyl in customers choice of color; clear vinyl windows on all three (3) side weather panels; top of each panel zippers to top canopy; bottom of panels include sewn on velcro straps to attach bottoms to frame; weather side panels zipper vertically to back panel corners; all panels can be rolled up and velcro strapped when not in use; zippers provide for easily removable panels

  - Model # DONKEY-WFP, Weather Front Panel; one (1) clear vinyl front panel; sewn on velcro straps attach to frame; panel rolls up and Velcro strapped when not in use; removable panel

  - Model # DONKEY-PFP, Weather Front Panel; one (1) clear plexi-glass front panel; framed in custom aluminum extrusion with rubber gasket attaches to top canopy  bolts; panel hinges up to canopy top when not in use; removable panel

  - Model # DONKEY-SC, Seat Cushion,18oz. vinyl encased 2" thick foam; 2” wide Velcro flap attaches cushion to aluminum plank; adds additional comfort

  - Model # DONKEY-BC, Backrest Cushion,18oz. vinyl encased 2" thick foam; 2" wide Velcro flap attaches cushion to aluminum plank; adds additional comfort

  - Model # DONKEY-PB, Penalty Bench; 10" wide aluminum plank with side and center support brackets; accommodates bottom front row seating for up to 6 people; typically used in the sport of lacrosse

  - Model # DONKEY-SP/PS, Premium Speaker Package with two (2) plug-and-play factory-installed seamless pre-wired outdoor speakers to unit

  - Model # DONKEY-MLS, Mounting Leg Supports; custom TIG welded legs with mounting plates allow unit to be secured semi-permanently to concrete columns poured and spaced per AAE spec drawings; this option removes the four (4) wheels and eliminates any portability of all three (3) DONKEY models

  - Model # DONKEY-TPG, Tinted Plexi Glass; surrounds three (3) sides of DONKEY units; two (2) side panels and one (1) back panel; offers a more permanent weather screen for personnel inside; all tinted plexi glass sections are framed with custom aluminum extrusion and bolt in place to frame; includes hinged lockable door on ladder entrance side

  - *Model No. DONKEY-BN - Bird’s Nest Filming Platform – 4'-0" x 4'-0" platform area with a 7'-0" platform height, TIG welded 4"sq. x .250" heavy-wall aluminum with rounded corners, TIG welded aluminum railing with 1-1/4"rd. aluminum spindles spaced 3-1/2" on center meets IBC Codes, two 16"diameter flat-free foam filled swivel casters with brakes, 12"wide x 4'-0" long anodized Referee’s Bench seat with backrest underneath platform, powder-coated aluminum canopy top color of choice, only to be used with DONKEY-1 & DONKEY-2 Models

  - *Model No. DONKEY-BN/10UP - Bird’s Nest Filming Platform – 4'-0" x 4'-0" platform area with an upgraded 10’-0" platform height, TIG welded 4"sq. x .250" heavy-wall aluminum with rounded corners, TIG welded aluminum railing with 1-1/4"rd. aluminum spindles spaced 3-1/2" on center meets IBC Codes, two 16"diameter flat-free foam filled swivel casters with brakes, 12"wide x 4'-0" long anodized Referee’s Bench seat with backrest underneath platform, powder-coated aluminum canopy top color of choice, only to be used with DONKEY-1 & DONKEY-2 Models

PART 3	EXECUTION

3.1  		INSPECTION

- Examine the areas and conditions where equipment and systems are to be installed and notify the contractor of conditions detrimental to the proper and timely installation and completion of the work.

- Do not proceed with the work until unsatisfactory conditions have been corrected by the contractor in a manner acceptable and to the satisfaction of the Architect/Engineer or Owner's Representative.

3.2	INSTALLATION

- All athletic equipment shall be installed as indicated on approved submittals as recommended and in strict accordance with manufacturer's written directions and as indicated on the drawings and specified herein.

- All athletic equipment shall be installed in strict accordance with the latest rules, regulations and specifications governing that sport or event for which it is being installed.

3.3  		TESTING, ADJUSTMENT AND OPERATION

- All athletic equipment requiring testing, adjustments and operation shall be tested for proper operation and adjusted to conform to specified standards.

- Provide certifications as required, indicating that equipment has been tested and adjusted to conform to specified standards.

- Provide operating and maintenance instructions and manuals to Owner -designated personnel for the proper operation and care of equipment after equipment has been tested and adjusted to conform to specified standards.

3.4  		CLEANING

- Upon completion of work in any given area, remove all trash and debris from the work area and leave in clean condition.

- END OF SECTION -