PART 1	GENERAL

1.1	SUMMARY

- Provide all equipment and materials, and do all work necessary to furnish and install the Track & Field Equipment, as indicated on the drawings and as specified herein.

1.2	RELATED WORK

- Examine Contract Documents for requirements that affect work of this section.  Other specification sections that directly relate to work of this Section include, but are not limited to:

  - Section 02200 - Earthwork; Excavation and Backfill and establishment of subgrade elevations.

  - Section 02511 - Asphalt Concrete Pavement

  - Section 02535 - Synthetic Track Surfacing

  - Section 02542 - Synthetic Field Surfacing

  - Section 03300 - Cast-in-Place Concrete; Concrete foundations and bases for goals.

1.3		REFERENCES

- Comply with applicable requirements of the following standards.  Where these standards conflict with other specified requirements, the most restrictive requirements shall govern.

      - U.S. Tennis Court and Track Builders Association

      - National Federation of State High School Associations (NFSHSA)

      - National Collegiate Athletic Association (NCAA)

      - International Amateur Athletic Foundation (I.A.A.F.)

      - Manufacturers Data and Recommended Installation Requirements.

1.4		SUBMITTALS

- Manufacturers Product Data

            - Provide manufacturer’s product literature, technical specifications and other data prior to actual field installation work for Architect or Owner’s Representative review.

# Shop Drawings

  - Provide drawings of manufacturers recommended installation and foundation requirements prior to actual field installation work for Architect or Owner’s Representative review.

1.5		QUALITY ASSURANCE

- Manufacturers warranties shall pass to the Owner and certification made that the product materials meet all applicable grade trademarks or conform to industry standards and inspection requirements.

1.6	DELIVERY, STORAGE AND HANDLING

- Materials delivered to the site shall be examined for concealed damage or defects in shipping. Any defects shall be noted and reported to the Owner’s Representative.

- Replacements, if necessary, shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- Sound materials shall be stored above the ground under protective cover or indoors so as to provide proper protection.

PART 2	PRODUCTS

2.1		MANUFACTURERS

- Manufacturers and product selections named are provided to establish the minimum standard.

      - Track & Field Equipment - As manufactured by AAE (Aluminum Athletic Equipment Co.); 1000 Enterprise Drive, Royersford, PA 19468; Toll Free (800) 523-5471.

2.2		Track & Field EQUIPMENT

- Pole Vault Standards and Accessories- Shall be as manufactured by AAE:

  - Model # PVS-HSX (high school model, NFHS) Pole Vault Standards meet and exceed all NFHS rule specifications, product consists of the following components: Standard Upright made of a custom heavy-wall 10’long aluminum extrusion with welded mounting plate with dual reinforcements, Standard Adjustment Post made of a 1-3/4”rd. heavy wall aluminum tube with a pre-attached Adjustment Body made of a custom heavy-wall aluminum extrusion vinyl-coated black with ergonomic star pattern rubber coated Adjustment Knob adjusts between 7’-0” (2.13 meters) and 21’-0” (6.4 meters) decal scale via Offset Arm made of a 1-1/4” diameter heavy-wall aluminum powder-coated safety yellow with four (4) crossbar locator pins made of  ½”diameter aluminum spaced 12” on center, Adjustment Bases made of ¼” HRS powder-coated dark grey with Hi-Performance™ base wheels and ½” diameter stainless steel axles, Aluminum Runway Frame with crossbar locator scale are made of custom aluminum extrusion 22”wide by 52”long with ¼”thick welded mounting straps to be anchored per NFHS specifications to a concrete pad via provided mounting hardware, all assembly hardware is stainless steel, Pole Vault Standards are sold as a pair and come with an AAE Lifetime Warranty

  - Model # PVS-NCAA (collegiate model, NCAA) Pole Vault Standards meet and exceed all NCAA rule specifications, product consists of the following components: Standard Upright made of a custom heavy-wall 12’long aluminum extrusion with welded mounting plate with dual reinforcements, Standard Adjustment Post made of a 1-3/4”rd. heavy wall aluminum tube with a pre-attached Adjustment Body made of a custom heavy-wall aluminum extrusion vinyl-coated black with ergonomic star pattern rubber coated Adjustment Knob adjusts between 7’-0” (2.13 meters) and 21’-0” (6.4 meters) decal scale via Offset Arm made of a 1-1/4” diameter heavy-wall aluminum powder-coated safety yellow with four (4) crossbar locator pins made of  ½”diameter aluminum spaced 12” on center, Adjustment Bases made of ¼” HRS powder-coated dark grey with Hi-Performance™ base wheels and ½” diameter stainless steel axles, Aluminum Runway Frame with crossbar locator scale are made of custom aluminum extrusion 22”wide by 52”long with ¼”thick welded mounting straps, frame to be anchored per NCAA specifications to a concrete pad via provided mounting hardware, all assembly hardware is stainless steel, Pole Vault Standards are sold as a pair and come with an AAE Lifetime Warranty

  - Model # PVS-IAAF (international model, IAAF) Pole Vault Standards meet and exceed all IAAF rule specifications, product consists of the following components: Standard Upright made of a custom heavy-wall 12’long aluminum extrusion with welded mounting plate with dual reinforcements, Standard Adjustment Post made of a 1-3/4”rd. heavy wall aluminum tube with a pre-attached Adjustment Body made of a custom heavy-wall aluminum extrusion vinyl-coated black with ergonomic star pattern rubber coated Adjustment Knob adjusts between 9’-0” (2.74 meters) and 21’-0” (6.4 meters) decal scale via Offset Arm made of a 1-1/4” diameter heavy-wall aluminum powder-coated safety yellow with two (2) crossbar locator pins made of  ½”diameter aluminum spaced 12” on center, Adjustment Bases made of ¼” HRS powder-coated dark grey with Hi-Performance™ base wheels and ½” diameter stainless steel axles, Aluminum Runway Frame with crossbar locator scale are made of custom aluminum extrusion 22”wide by 52”long with ¼”thick welded mounting straps, frame to be anchored per IAAF specifications to a concrete pad via provided mounting hardware, all assembly hardware is stainless steel, Pole Vault Standards are sold as a pair and come with an AAE Lifetime Warranty

  - Model # ARF-52 (for all model standards) Aluminum Runway Frame should be specified when there are multiple pole vault pad locations additional runway frames should be specified Aluminum Runway Frame with crossbar locator scale are made of custom aluminum extrusion 22”wide by 52”long with ¼”thick welded mounting straps, frame to be anchored per NCAA specifications to a concrete pad via provided mounting hardware, all assembly hardware is stainless steel, runway frames are sold as a pair and come with an AAE Lifetime Warranty

  - Model # PVS-AW (for all model standards) Anchor Weight should be specified when concrete anchor pads cannot be used for anchoring runway frames, product consists of a 3/16” thick HRS 3’ x 4’4” anchor plate vinyl-coated black with stainless steel attachment hardware, Pole Vault Standard Anchor Weights are sold as a pair and come with an AAE Lifetime Warranty

  - Model # PVS-PAD (for all model standards) Standard Pads  should be specified to help provide additional safety for athletes attach to the pole vault standards, product consists of 1”thick x 72”high pad encased in an 18oz. vinyl in high visibility safety yellow attaches to standard via five (5) buckle straps, Pole Vault Standard Pads are sold as a pair

  - Model # XG5 (for all model standards) Pole Vault Crossbar should be specified as an item required for the pole vault event used with the pole vault standards, product consists of 1 ¼”diameter x 14’-10”long high visibility yellow round fiberglass with dual target area red stripes for athletes reference in air, includes dual vinyl crossbar ends with flat bottom for resting on pole vault standard’s crossbar pins, Pole Vault Crossbars are sold individually

  - Model # ALT-20 (for all model standards) Crossbar Lifter should be specified to assist official’s helpers in placing the crossbar to higher heights, product consists of 1”diameter telescopic three (3) tier aluminum pole twist-lock extends to reach up to 20’ from ground level, welded lifter device with pivot action at end to seat crossbar and ease raising crossbar and seating properly on offset bar pin, Pole Vault Crossbar Lifters are sold individually

  - Model # AMB-6 (for all model standards) Aluminum Measuring Bar should be specified to assist official’s in accurately measuring the crossbar height in the middle, product consists of 1 ½”square telescopic three (3) tier aluminum with pre-attached scales with a welded ¾”diameter by 12”long aluminum measuring bar that extends up to 20’ (6 meters) to reach crossbar when standards bases are brought in on the runways frames to 0” location, Aluminum Measuring Bars are sold individually

  - Model # SSVB (for all model standards) Stainless Steel Vault Box should be specified as an item required for the pole vault event, product consists of 13 gauge (.090”) formed 304 stainless steel sheet with welded anchor collars, meets NFHS, NCAA and IAAF specifications, unit is to be set in concrete according to manufacturer’s specifications, Vault Boxes are sold individually

*NOTE: See AAE specifications for Pole Vault Landing Pads to specify proper padding mandatory for the pole vault event.

PART 3	EXECUTION

3.1  		INSPECTION

- Examine the areas and conditions where equipment and systems are to be installed and notify the contractor of conditions detrimental to the proper and timely installation and completion of the work.

- Do not proceed with the work until unsatisfactory conditions have been corrected by the contractor in a manner acceptable and to the satisfaction of the Architect/Engineer or Owner's Representative.

3.2	INSTALLATION

- All athletic equipment shall be installed as indicated on approved submittals as recommended and in strict accordance with manufacturer's written directions and as indicated on the drawings and specified herein.

- All athletic equipment shall be installed in strict accordance with the latest rules, regulations and specifications governing that sport or event for which it is being installed.

3.3  		TESTING, ADJUSTMENT AND OPERATION

- All athletic equipment requiring testing, adjustments and operation shall be tested for proper operation and adjusted to conform to specified standards.

- Provide certifications as required, indicating that equipment has been tested and adjusted to conform to specified standards.

- Provide operating and maintenance instructions and manuals to Owner -designated personnel for the proper operation and care of equipment after equipment has been tested and adjusted to conform to specified standards.

3.4  		CLEANING

- Upon completion of work in any given area, remove all trash and debris from the work area and leave in clean condition.

- END OF SECTION -